Orchard robot project

Webcam setup:

I. We need to install the ROS driver:

1. Check for device connection:
$ ls /dev/ | grep video
If this shows video0 then the usb cam is successfully connected.

2. install ROS webcam driver called usb_cam:
$ sudo apt-get install ros-kinetic-usb-cam
(for other versions of ROS such as jade use $ sudo apt-get install ros-jade-usb-cam)

https://www.packtpub.com/mapt/book/hardware_and_creative/9781783551798/8/ch08lvl1sec60/interfacing-usb-webcams-in-ros

3. Package for the webcam driver is obtained from github, this contains all the documents nesccary for the webcam setup.
http://wiki.ros.org/usb_cam
NOTE: In ROS wiki it installs the driver using $ rosdep install camera_calibration which is basically the same as using $ sudo apt-get install ros-kinetic-usb-cam.

With the webcam driver downloaded from github there is a launch file that can executed using roslaunch command, this switches on the webcam. Warning occur in the command line showing the webcam is uncalibrated. Therefore next step is to calibrate the webcam.

[ WARN ] : Camera calibration file /home/..../.ros/camera_info/head_camera.yaml not found

[ WARN ] : unknown control 'focus_auto'
II. After the driver is installed we need to calibrate the camera:

This link goes to a book for a quick introduction and basics into ROS:
https://www.cse.sc.edu/~jokane/agitr/